## Slide 1: Clinical and Epidemiologic Research:
Sample
Measure
(Intervene)
Analyze
Infer
Notes: Remember from last week how we broke down clinical and epidemiologic research into its most basic elements. We sample human subjects, make measurements on them, sometimes intervene, analyze the relationships of these measurements, and then make inferences. Last week we focused on how problems in sampling can threaten the validity of our studies; this is manifested in what we called selection bias. Today, we’ll begin the first of two sessions on measurement, and a strong argument can be made that measurement is the most important element. For example, even in order to sample human subjects, it is usually the case that we have to make some kind of measurement on them first. So, measurement is important in clinical research starting at the very beginning of studies.

## Slide 2: A study can only be as good as the data . . .
-J.M. Bland
i.e., no matter how brilliant your study design or analytic skills you can never overcome poor measurements.
Measurement is so important that we will:
Dedicate an entire session to it per se
Go well beyond the text
Have you read a few original methodologic articles
Notes: JM Bland, the co-author of today’s readings, said it best in his textbook “A study can only be as good as its data. . . .”
i.e. no matter how brilliant your study design or analytic skills you can never overcome poor measurements.
Unfortunately, measurements are often the most neglected part of the list I just mentioned, and this is why we are going to spend a whole session talking about measurement per se. To do so, we are going a little out of order in the text and also add several articles written by Bland and Altman who I think are among the clearest thinkers on the subject. We’re giving you these original articles because no textbook explains this material as well as these articles. These are articles we believe you should be able to understand. Like everyone else, you may need to read them more than once, but they actually are very clear. The other reason we are giving you these articles is to point out to you that there is a methodological literature out there that you should be aware of. Clinical research methods aren’t stagnant and like every other field it is important to keep up as they change.

## Slide 3: Understanding Measurement: Aspects of Reproducibility and Validity
Reproducibility vs validity of measurements
Focus on reproducibility: Impact of imperfect reproducibility on precision & validity of study inferences
Quantitating reproducibility of interval scale measurements
  Depends upon purpose
    Research
      intraclass correlation coefficient
    Individual use
      within-subject standard deviation and “repeatability”
      coefficient of variation
Improving reproducibility
(Estimating validity of measurements -- On Problem Set)
Notes: Here is our roadmap for today for our discussion of measurement.
We’ll first discuss the two main characteristics of a measurement, its reproducibility and its validity. We’ll then spend the rest of the time focusing on reproducibility and, in particular, explain the impact of reproducibility on validity and on precision of the inferences in your studies. We will discuss how you can numerically estimate the reproducibility of your measurements and talk about how this is done according to the purpose, either research or individual patient-level management. We will describe the intraclass correlation coefficient for when the purpose is research, and, for when individual use is the goal, we will discuss the within-subject standard deviation, and its most useful derivative, repeatability, as well as the coefficient of variation.
We will then end the session by talking about some practical tips to improve reproducibility.
Although we won’t discuss validity here in class today, we will assess the validity of measurements in the Problem Set for this week.

## Slide 4: Measurement Scales
Notes: Before we get into the heart of the material today, we need to review measurement scales or measurement types to make sure you understand the terminology I am using. I have broken up things into interval and categorical scales. Interval scale means that the difference between each unit on the scale is the same no matter where you are on the scale; for example, for weight the difference between 150 lbs and 149 lbs is the same as between 5 lbs and 4 lbs. The values that can be observed when using a continuous scale, like measuring weight, are only limited by the mechanical sensitivity of the instrument. On a discrete interval scale, there are a limited number of values like, for example, when measuring white blood cell count where values are limited to integers.
Categorical scales refer to assigning measurements to categories only, and there is not necessarily the same relationship between each of the categories as there is between units for variables measured with an interval scale. For example, many tumors have staging systems, say like 1,2,3,4 but the difference between stage 4 and stage 3 is not necessarily the same as between stage 3 and stage 2. There is order, however, in tumor staging: 4 is worse than 3 which is worse than 2 and hence such a scale is called an ordinal scale. Nominal scales have no order. Race or religion are examples. Finally, a dichotomous scale has only two values (yes or no, present or absent).

## Slide 5: Reproducibility vs Validity of a Measurement
Reproducibility
  the degree to which a measurement provides same result each time it is performed on a given subject or specimen
  less than perfect reproducibility caused by random error
Validity
  from the Latin validus – strong
  the degree to which a measurement truly measures (represents) what it purports to measure (represent)
  less than perfect validity is fault of systematic error
Notes: Let’s start our discussion of reproducibility and validity by going over some basic definitions that I think you are familiar with. Reproducibility refers to the degree a measurement provides the same result each time it is performed on a given subject or specimen. If you are measuring something over and over with the same technique, we say that anything less than perfect reproducibility is caused by random error.
In contrast, validity is from the Latin validus meaning strong. It is the degree to which a measurement truly measures (represents) what it purports to measure (represent). We say that anything less than perfect validity is the fault of systematic error.

## Slide 6: Synonyms: Reproducibility vs Validity
Reproducibility
  aka: reliability, repeatability, precision, variability, dependability, consistency, stability
  “Reproducibility” is most descriptive term: “how well can a measurement be reproduced”
Validity
  aka: accuracy
Notes: Unfortunately, as in so many parts of clinical research, the literature is replete with other terms for reproducibility and these include reliability, repeatability, precision, variability, dependability, consistency, stability. Today, I will stick with the term I think is best - reproducibility. It is the most descriptive because it asks “just how well can the measurement be reproduced.”
Thankfully, there are not too many synonyms for the concept of validity, but you will find the word accuracy used in this context.

## Slide 7: Vocabulary for Error
 | Overall Inferences from Studies (e.g., risk ratio) | Individual Measurements
Systematic Error | (Last Week) Validity | (This Week) Validity (aka accuracy)
Random Error | Precision | Reproducibility
Notes: Remember from last week, we talked about systematic and random error in the context of overall inferences (for example, odds ratios or risk ratios) from studies. We talked about validity capturing the degree of systematic error and the term precision capturing the degree of random error.
This week we are dealing with very similar concepts but we are talking about individual measurements of either exposure variables or outcome variables (or any other type of variable, such as a confounding variable). For individual measurements of variables, we again talk about validity (although sometimes you’ll hear the term accuracy) when referring to how far off the measurement is from the truth, in other words, the degree of systematic error, but we’ll use the term reproducibility when talking about the random error.

## Slide 8: Reproducibility and Validity of a Measurement
Good Reproducibility
Poor Validity
Poor Reproducibility
Good Validity
Consider having 5 replicates (aka repeat measurement) (eg, height)
Notes: Remember these figures from last week in the context of having five different attempts at estimating an overall inference in a study by drawing 5 different samples. This week, we’ll consider these figures in the context of making an individual measurement on a subject or a biological specimen. Consider that we are attempting to measure the truth about a particular aspect of a given individual (say, it’s his height) and we are given five tries. The center of the diagram represents truth. Here we have five replicates - a term which means repeated measurement - which are closely bunched, i.e. reproducible but they are off target so they have poor validity. Here, the replicates are all over the place, i.e. poor reproducibility but their average is right on target so they are considered to have good validity

## Slide 9: Reproducibility and Validity of a Measurement
Good Reproducibility
Good Validity
Poor Reproducibility
Poor Validity
Notes: Of course, what you want is this - good reproducibility and good validity and what you want to avoid is this - poor reproducibility and poor validity

## Slide 10: Understanding Measurement: Aspects of Reproducibility and Validity
Reproducibility vs validity of measurements
Focus on reproducibility: Impact of imperfect reproducibility on precision & validity of study inferences
Quantitating reproducibility of interval scale measurements
  Depends upon purpose
    Research
      intraclass correlation coefficient
    Individual use
      within-subject standard deviation and “repeatability”
      coefficient of variation
Improving reproducibility
(Estimating validity of measurements -- On Problem Set)
Notes: Now that we have defined and contrasted reproducibility and validity of measurements, we will spend the rest of the day focusing on reproducibility. We will start by focusing on the impact of imperfect reproducibility on the things you do downstream with the measurement, meaning an impact on the precision and validity of study inferences.
We’ll then talk about quantitating reproducibility and improving it.
We aren’t ignoring validity. Instead, you will have chance to get practice with validity of measurements in this week’s Problem Set.

## Slide 11: Impact on Precision of Inferences Derived from Measurement (and later: Impact on Validity of Inferences derived from measurement)
Classical Measurement Theory:
  observed value (O) = true value (T) + measurement error (E)
  If we assume E is random and normally distributed:
    E ~ N (0, 2E)
  Mean = 0
Fraction
error
-3
0
.02
.04
.06
Error
-2
-1
0
1
2
3
Distribution of random measurement error
Why Care About Reproducibility?
  Variance = 2E
Notes: Why make a fuss over reproducibility? There are two reasons: the first is that it can have a big impact on the statistical precision of the inferences you go on to make with these measurements (like when you correlate one measurement with another and get things like risk ratios and odds ratios and the like). The second reason is that it can have a big impact on the validity of your studies. We’ll get to validity in a minute; let’s first talk about the impact of reproducibility on precision.
To understand the impact of reproducibility of a measurement on the precision of inferences, we need to look at a little bit of classical measurement theory:
We would all agree that when we make a measurement on someone with a valid measurement tool the observed value we obtain is the combination of the true underlying value and some measurement error. We will assume here – and it is a reasonable assumption -- that this measurement error is random and also make the very reasonable assumption that it is normally distributed. Graphically, with these assumptions, if we were able to make a zillion replicate measurements of something, say weight or height, on a given person, this is what the distribution of the error term would look like. The majority of the errors are clumped around zero and the mean is zero. As we move away from zero, we see a smaller frequency of errors. The variance of this distribution is known as sigma squared sub E. Sigma squared is the notation we use for the variance of a distribution and sigma alone is the standard deviation. I know you have discussed the mean and the variance of a distribution in the Biostats I course.
(The notation we use is that measurement error, which we call E, is distributed (that’s the tilda), normally (depicted with an N) and that it has a mean of zero (the first number in the parentheses) and some variance, signified by sigma squared subscript E, which is the second number in the parentheses. )

## Slide 12: Impact of Reproducibility on Precision of Inferences
What happens if we measure, e.g., height, on a group of subjects?
Assume for any one person:
  observed value (O) = true value (T) + measurement error (E)
  E is random and ~ N (0,  2E)
Then, when measuring a group of subjects, the variability of observed values ( 2O ) is a combination of:
  the variability in their underlying true values ( 2T )
  and
  the variability in the measurement error ( 2E)
  2O = 2T + 2E
Between-subject variability
Within-subject variability
Notes: What happens when we jump from measuring one person to measuring a group of people, as is our usual practice in clinical research? Let’s say we are measuring height.
Assuming that measurement error is random and normally distributed, then the variability of observed values in the group - again depicted by its variance (sigma squared subscript O) - is a combination of the variability of the true values in the group subjects (sigma squared subscript T) and the variability in the measurement errors (sigma squared subscript E)
Sigma squared observed = sigma squared true values plus sigma squared for the error
variance of the observed values = variance in the true values and the variance in the errors
We won’t mathematically formally prove this so I will ask you to accept it at face value. However, at face value it does make a lot of sense.
Another way to see this is that overall variability of a group is the sum of true between-subject variability and within-subject variability (which is caused by measurement error). We will use these terms synonymously. In other words, sigma squared sub T is equal to between-subject true variability and sigma squared sub E is equal to within-subject variability.

## Slide 13: Why Care About Reproducibility?
2O = 2T + 2E
More random measurement error when measuring an individual means more variability in observed measurements of a group
  e.g., measure height in a group of subjects.
  If no measurement error
  If measurement error
Height
Frequency
Distribution of observed height measurements
Notes: So, this is a handy equation to know. It obviously follows that the more random measurement error you have when measuring an individual subject (i.e. the wider the variance of the measurement error) then the more variability you are going to see in your observed measurements when looking at a group of persons.
For example, what if you measured height in a group of research subjects? If there was no measurement error and all you had to deal with was the underlying variability in the true heights of the participants, the distribution or variability of the heights might look like this. However, if you also have to deal with measurement error, then there is an extra source of variability and now the observed variability in height will look like this. In other words, there is more overall variability.

## Slide 14: More variability of observed measurements has important influences on statistical precision/power of inferences
2O = 2T + 2E
Descriptive studies: wider confidence intervals
Analytic studies (Observational/RCT’s): power to detect an exposure (treatment) difference reduced for given sample size
truth
truth + error
truth
truth + error
Confidence interval of the mean
Confidence interval of the mean
Exposed
Unexposed
Notes: Why is this important? It is important because more variability in the observed measurements has important influences on statistical precision in all study designs. In descriptive studies, more variability means wider confidence intervals. If your goal is to estimate the mean height, for example, in a given population, then more variability in the observations leads to a wider confidence interval in the estimated mean, shown here. In other words, less certainty as to what the true value is. This is unfavorable.
In analytic studies, be it observational or experimental trials, more variability translates to less power, for a given sample size, to see if a given predictor variable is associated with an outcome variable. This is depicted here in that when measurement error increases, the variability of measurement within two groups under study increase. Distinguishing between these two means in the left panel, the mean of this group and the mean of this group, is much easier (i.e. you have more power) than distinguishing these two means in the right panel. The more variability you have in groups, the less power you have to detect a given difference in the means of the two groups for any given sample size. Again, this is a problem in observational or experimental interventional studies.
So, no matter what kind of work you do there is no escaping the unfavorable influences of measurement error.

## Slide 15: Effect of Variance (2O) on Statistical Power
e.g., evaluation of skin fold thickness in 2 groups
Effect size = 0.4 units
100 subjects in each group
Alpha = 0.05
Standard deviation of skin fold thickness
(square root of the variance in the study population)
Notes: Let’s look formally at how the variability of a measurement influences statistical power. Those of you who played around with the effects of changing standard deviation for an outcome variable in your sample size calculations for your summer protocol are very aware of this. Here is a scenario where we are evaluating means of, say, skin fold thickness, in 2 groups and the desired effect size is 0.4 (the units don’t even matter). Let’s say that we have 100 subjects available to us in each group. If the standard deviation of the outcome variable is 1 (which is the same as a variance of 1), then we would have a respectable 80% power. What if the standard deviation of the outcome variable is 2 (equivalent to a variance of 4). Now, power is about 30%. Don’t even bother going forward in your research study with this scenario.

## Slide 16
Many researchers are aware of the influence of too much variability in a study variable
Fewer wonder how much of variance is due to:
  random within-subject measurement error (2E)
  vs
  true between-subject variability (2T)
Notes: Most of you have already appreciated the influence of too much variability in a study variable, but how many of you have wondered how much of this variance (or standard deviation) in a study variable is due to random measurement error vs true between-subject differences?

## Slide 17: Why Care About Reproducibility?
Impact on Validity of Inferences Derived from Measurement
Consider a study of height and basketball shooting ability:
  Assume height measurement: imperfect reproducibility
  Imperfect reproducibility means that if we measure height twice on a given person, most of the time we get two different values; at least 1 of the 2 individual values must be wrong (imperfect validity)
  If study measures everyone only once, errors, despite being random, will lead to biased inferences when using these measurements (i.e. inferences have imperfect validity)
Notes: So, that is the influence of reproducibility on precision of study inferences. How about the impact on validity of inferences derived from measurements? We are going to say more about this next week in our session on measurement bias, but let’s go through a simple example now.
Consider a simple study looking at the association between height and basketball shooting ability. Assume that we are working with a measurement of height that has imperfect reproducibility. Imperfect reproducibility means that if we measure height twice on a given person we will most of the time get two different values. That means that one of the two individual values must be wrong (i.e. imperfect validity).
When we actually do our study, if we make the measurement only once on everyone, as is common practice, the errors in the measurement, despite being random, can result in biased inferences when we start to look at the association with basketball-shooting ability. In other words, the lack of reproducibility leads to getting an answer that will differ from the true answer, i.e. inferences that have imperfect validity.

## Slide 18
Measurement Bias
More next week
Notes: Let’s work through some numbers. Again, we are interested in determining the relationship between height and ability to shoot a basketball. Say that you make a cutoff of 6 feet to designate a tall person. Let’s say that height is indeed truly associated with basketball ability; say that tall persons are one and 1/2 times more likely to be good basketball shooters. This is what a 2x2 table would look like if this were the case and if everything was measured with perfect reproducibility and validity. If we did a study of 100 persons, 10 of 40 of those above 6 feet are found to be good shooters compared to 10 of 60 of those below 6 feet. This amounts to a prevalence ratio of 10/40 div by 10/60 or 1.5. If, however, our measurement of height is not perfectly reproducible and that when we measure everyone only once, let’s assume that we will misclassify 10% of individuals. That is, we will have 10% of those truly tall being classified as short and 10% that are truly short being classified as tall. Because this is a random error, this will happen to the same degree in the good shooters versus the poor shooters. You see here how the cells begin to change in the presence of this misclassification. Among the good b-ball players, one truly tall person is mistakenly called not tall and one truly not tall person is mistakenly called tall. Among the poor b-ball players, 10%, or 3, of the tall players are mistakenly called not tall and 5 of the 50, again 10%, not tall persons are classified as tall. The net effect of this measurement error is shown here in this 2x2 table. The association that you find in your study will be blunted or attenuated in reference to the truth, i.e. biased. The truth is that tall persons are 1.5 times more likely to be good basketball shooters. What you observed, however, is that tall persons are only 1.38 times more likely. The point is that imperfect reproducibility of height, i.e. random measurement error, can lead to biased inferences, in other words, wrong answers – in a predictable direction. Next week, we will cover the effects of random measurement error on validity in even more detail, but suffice it to say for today that lack of reproducibility has an important impact on validity .

## Slide 19: Understanding Measurement: Aspects of Reproducibility and Validity
Reproducibility vs validity of measurements
Focus on reproducibility: Impact of imperfect reproducibility on precision & validity of study inferences
Quantitating reproducibility of interval scale measurements
  Depends upon purpose
    Research
      intraclass correlation coefficient
    Individual use
      within-subject standard deviation and repeatability
      coefficient of variation
Improving reproducibility
(Problem set: assessing validity of measurements)
Notes: Let’s pause for a moment to see where we are: We have defined reproducibility and validity of measurements and focused on reproducibility in terms of its influence on precision and inferences. Let’s now discuss how we actually calculate, or express, reproducibility.

## Slide 20: Numerical Estimation of Reproducibility
Many options in literature, but choice depends on purpose/reason and measurement scale
Two main purposes/reasons to estimate reproducibility:
  Research: Should more effort be exerted to further optimize reproducibility of the measurement?
  Individual (clinical) use: Just how different could two measurements taken on the same individual be -- from random measurement error alone?
Notes: How do we go about actually estimating reproducibility - in other words, put it into a number?
There are actually many options described in the literature. In fact, it is a dizzying array with little guidance as to when to use each metric. However, the choice depends on the purpose or reason you have in mind when assessing reproducibility and, of course, the measurement scale.
We contend that there are two main reasons to estimate reproducibility. The first reason comes up in research. It is the question of how much more effort should be exerted to further optimize/improve the reproducibility of the measurement? The second reason comes up in individual patient or clinical management or classification, which although not the focus of this course, is an important goal and gives information about the inherent reproducibility of the measurement that most observers can relate to. For this purpose, the question is: Just how different could two measurements taken on the same individual be – from random measurement error alone?

## Slide 21: Estimating Reproducibility of an Interval Scale Measurement: Example: A New Method to Measure Peak Flow
Purpose of calculation: Should more effort be given to enhance reproducibility for use in research?
Assessment of reproducibility requires >1 measurement per subject
Peak Flow in 17 young adults
(modified from Bland & Altman)
Notes: Let’s consider an example of an interval scale measurement. Consider that we are evaluating a new method to measure peak expiratory flow, a measure of how fast you can expire (i.e. blow out of your mouth). And, let’s consider that our goal or purpose is to see whether we need to improve the reproducibility of this measurement for use in research.
To assess reproducibility it should go without saying that we need to make more than one measurement on each subject. This is actually perhaps not so obvious to everyone as Bland and Altman point out in some of their other work where they describe many examples of authors attempting to describe the reproducibility of a measurement despite having made only one measurement per subject. There is a distinct science to designing studies to estimate reproducibility, which we won’t cover in detail in this course. Rather, we will work on understanding the results of such studies.
Here is the structure of the data: 17 subjects and two measurements a piece for each subject.
How should we approach assessing the reproducibility of Peak Flow?

## Slide 22: A Mathematical Definition of Reproducibility
Reproducibility
Varies from 0 (poor) to 1 (optimal)
As reproducibility approaches 1, variability is virtually all between-subject
  Little room/need to diminish within-subject random error
  Not much you can do with the measurement to decrease observed variability (but you could work on the subjects)
Notes: To better understand the impact of reproducibility on our inferences in our estimates in research studies and whether we should work to improve reproducibility, here is a mathematical definition of reproducibility.
Reproducibility is the fraction of the total observed variance, when measuring a group of subjects, that is accounted for by the variability in the true values. If all the variance in your measurements that you see is simply because the things you are measuring are inherently that variable, then you have complete 100% reproducibility. Thinking about reproducibility like this, it then varies from 0 (poor) to 1 (optimal). Looking at this equation, as measurement error becomes small (i.e., goes to zero), this term leaves the denominator and you end up with sigma squared of the true values divided by itself, or 1.
Another way to think about this is that 1 minus reproducibility, which is sigma squared sub E over sigma squared sub 0, is the fraction of overall variability attributed to random measurement error.
Again, it is important to be sure about your purpose. The question that was posed in the last slide was “Do we need to improve the reproducibility of this new method for use in research?”.
Remember that as reproducibility approaches 1, the variability is virtually all between-subject. This means that there is very little room or need to diminish within-subject random error; there is not much you can do to improve the reproducibility. If you wanted to decrease overall variability in the measurement, you would have to work on getting a more homogeneous sample of subjects.

## Slide 23: ICC
Think of as ratio
  Spread of True Signal between people to
  Spread of (True Signal + Noise)
In research, our goal is to be able to distinguish between people when they are truly different.
Hence, we want the ICC, which is spread of true signal compared to total, to be very high
Intraclass correlation coefficient (ICC)
Notes: This mathematical expression is called the intraclass correlation coefficient, or ICC. This is not exactly an intuitive name nor is it commonly understood, but it is nonetheless very meaningful. Note that it is important to include the “intraclass” distinction in the name. In contrast, the interclass correlation coefficient is the less commonly used name for the commonly known Pearson correlation coefficient, the most common parametric correlation test.
Think of the ICC as a ratio; it is a ratio of the spread of the true signal between people to the spread of the total signal plus all of the noise. In research, our goal is to be able to distinguish between people when they are truly different. That said, when you have the spread of the true values between people you sure don’t want it to be dwarfed by the noise in the measurement. Hence, you want the ICC ratio to be very high, i.e., for most of the total spread in the data to be attributable to the true spread between people.

## Slide 24: Intraclass Correlation Coefficient (ICC)
ICC
. loneway peakflow subject
  One-way Analysis of Variance for peakflow:
  Source SS df MS F Prob > F
  -------------------------------------------------------------------------
  Between subject 404953.76 16 25309.61 108.15 0.0000
  Within subject 3978.5 17 234.02941
  -------------------------------------------------------------------------
  Total 408932.26 33 12391.887
  Intraclass Asy.
  correlation S.E. [95% Conf. Interval]
  ------------------------------------------------
  0.98168 0.00894 0.96415 0.99921
Interpretation of the ICC?
Calculation explained in S&N Appendix; available in “loneway” command in Stata (set up as ANOVA)
98% of the total variability is due to inherent true between-subject variability and only 2% is due to within-subject random measurement error.
Notes: The ICC is the fraction of the total variability that is explained by the true between-subject variability. If all of the variability in observed measurements in a group of subjects is simply because of the inherent differences between subjects and none of it is because of measurement error, then reproducibility will be 1.
We are not going to dwell on how to calculate the ICC. It turns out that there are about six slightly different flavors and some of this is explained in the appendix in the S and N textbook. In Stata, the ICC is most easily determined when setting up the data as you would for an ANOVA (analysis of variance). When we do this, we find that the ICC for this new measurement is 0.98.
What does this 0.98 mean? It means that 98% of the total variability in the peak flow measurements is due to inherent true between-subject variability and only 2% is due to within-subject random measurement error.

## Slide 25: ICC for New Peak Flow Measurement
Should you do more work to optimize reproducibility of this measurement before it is used in your research?
No. Good to go! - A
Need more information - C
More optimization needed- B
ICC = 0.98
Notes: 25
What do we think of the ICC of 0.98?
Should more work be done to optimize reproducibility of this measurement before it is used in research?

## Slide 26: ICC for New Peak Flow Measurement
No. Good to go! - A
Need more information - C
More optimization needed- B
ICC = 0.98
Should you do more work to optimize reproducibility of this measurement before it is used in your research?
Notes: 26
0.98 sounds very high, and thus sounds like excellent reproducibility, but it turns out that you need more information.

## Slide 27: ICC for Peak Flow Measurement
ICC = 0.98
Caveat for interpreting an ICC:
  For any given level of random error (2E), ICC will be larger as 2T is larger, and smaller as 2T is smaller
  ICC only relevant in population from which data are representative sample (i.e., ICC is population dependent)
Implication:
  You cannot use any old ICC to assess your measurement.
  ICC measured in a different population than yours (i.e., smaller or larger 2T ) will not be relevant to you
  You need to know the population from which an ICC was derived
Notes: So, the ICC for the peak flow data is 0.98. What does this tell us? Is this new measurement suitable for research? Or, stated as we did before, should more work be done to optimize reproducibility of this measurement for research?
Before you answer this, there is one caveat to point out about the ICC. Note that in its calculation, that for any given level of random error, the ICC will be larger if the true between-subject variability is larger and smaller as the between-subject variability gets smaller. That said, this ICC that we calculated will only be relevant in a population that had this between-subject variability.
What is the implication of this? It is that you cannot use any old ICC that you find in the literature to assess your measurement. You need to know the population from which it was derived and whether that population is similar to the one you are studying. Any given ICC value, because it is so dependent upon the variability of true between-subject spread, is only relevant to the population it was derived in.
If this ICC of 0.98 was derived in a population that we will be studying in your research, then the value of .98 indicates that you would not gain much by optimizing its reproducibility. If this ICC was derived in a population with greater variability than your population, then the ICC is going to be even higher and hence we don’t need further optimization. If this ICC was derived in a population with less variability than your population, then we aren’t so sure. We will need to do some further exploration of just how different the two populations are.

## Slide 28
Overall observed variance (s2O ~ 2O)
Exploring the Dependence of ICC on Overall Variability in the Population
Notes: Let’s explore the dependence of ICC on the overall variability in the population. We can determine the overall variance in the peak flow data in ways you already know how to do. This is a simple calculation of variance.
It turns out to be 12392.

## Slide 29: Impact of 2O on ICC
Scenario | 2O | 2E | ICC
Peak flow data sample | 12,392 | 234 | 0.98
More overall variability | 20,000 | 234 | 0.99
Less overall variability | 1200 | 234 | 0.80
When planning studies, to understand if further optimization is needed of a measurement’s reproducibility:
  need to evaluate an ICC from a similar population as yours; or
  estimate what the ICC will be in your study population
Notes: So, for the peak flow data, the overall observed variance is 12,392. In calculations we will explain later, the sigma squared sub E, the within-subject variability, is 234. 234 divided by 12392 is 0.98, which is what we calculated before.
Now, let’s understand the impact of this new peak flow measurement when used in other populations. Let’s say we are performing research with a population with even more overall between-subject variability, where let’s say the overall variance is 20,000. Now the ICC is going to be even higher, 0.99, and there is even less influence from the error term. Nothing about the goodness of the measurement changed but we are simply using it in a population that has more variability. So, in this population, problems with reproducibility are negligible and you really don’t have to spend any time optimizing the reproducibility of the measurement. However, what if we were studying a much more homogenous population where the overall variance was 2000. Now the impact of the error term is higher and the ICC is 0.80, in other words, 20% of the variability is due to random measurement error. Now, for example, you might want to do something (e.g., begin taking replicate measures) to improve reproducibility.
The conclusion of these calculations is that when planning research studies, in order to understand if further optimization is needed of a measurement’s reproducibility, it is important to evaluate a previously established ICC from a similar population or, if this is not available, make an estimate of what the ICC will look like in your proposed study population.

## Slide 30: Dependence on ICC on Between-subject Variability
Is this dependence a limitation of the ICC?
Wouldn’t it be better just to have 1 number for measurement reproducibility you could use everywhere?
Answer: No
In research:
  goal is to distinguish between subjects when there is truly a difference (seeing signal above the noise)
  therefore, the question for our measurement is whether it is good enough to distinguish -- the ICC helps to tell us this
If difference between subjects is truly great, then only a crude measurement tool is all you need
ICC provides info on reproducibility of the measurement in the context where it is being used
Notes: Sometimes people have asked whether this dependence on population a limitation of the ICC? In fact, some writings indicate that it is a limitation. After all, wouldn’t it be better to just have 1 number that we could use to quantitate reproducibility that we could use in all contexts?
The answer is no. This is because in research our goal is to be able to distinguish between subjects when there is truly a difference between them. In other words, we want to be able to tell signal above noise. Therefore, we need to know if our measurement is good enough to make this distinction. Thankfully, the ICC tells us this.
Stated another way, if the difference between subjects is truly great, then only a crude measurement tool is needed to tell them apart. On the other hand, if the difference between subjects is small, then you need a very sharp tool. The ICC tells us how sharp our tool is.

## Slide 31: ICC for Peak Flow Measurement
ICC = 0.98
Is this suitable for research? Should more work be done to optimize reproducibility of this measurement?
If peak flow measurement will be studied in a population with similar (or greater) 2T as the population where ICC was derived, then no further optimization of reproducibility is needed
Notes: So, what is the bottomline for this new peak flow measurement?
If peak flow measurement will be studied in a population with similar (or greater) 2T as the population where ICC was derived, then the ICC of 0.98 is relevant and therefore no further optimization of reproducibility is needed.

## Slide 32: Some other ICC’s
Chambless AJE 1992. Point estimates and confidence intervals shown.
Reproducibility of lipoprotein measurements in the ARIC study
ICC
ARIC is a nationally representative sample of U.S. adults
Notes: Here are few more real-life examples of ICC, as shown in your textbook.
These are ICCs for lipoprotein measurements from the population-based ARIC study, which is a nationally representative cohort of adults in the US. ARIC stands for Atherosclerosis Risk in Communities. Because these are derived from population-based samples, they can be considered representative of the general population. You can see how they vary widely.

## Slide 33: Interpreting ICCs
You are planning a study of these analytes in African-American girls in San Francisco.
Just APO A-1 - A
Need more information - E
All of them - C
None of them - B
Those whose CI is > 0.10 units - D
ICC
For which analyte(s) should you consider improving reproducibility?
Notes: 33
Let’s ask a question. Let’s say that you are planning to do study of these biochemical analytes in African-American girls in San Francisco. For which of them should you consider improving reproducibility? Is it …..

## Slide 34: Interpreting ICCs
You are planning a study of these analytes in African-American teenagers in San Francisco.
Just APO A-1 - A
Need more information - E
All of them - C
None of them - B
Those whose CI is > 0.10 units - D
ICC
For which analyte(s) should you consider improving reproducibility?
Notes: 34
The best formal answer is that you need more information. Specifically, you really don’t know what the overall observed variability will be in African-American girls. Formally, the overall variability might be smaller or it might be larger. You really don’t know until you measure it (or if we tell you). However, it is also reasonable to infer that because this is a narrower population, the overall variability will be smaller and hence the ICC will only be lower. In other words, these ICCs from ARIC came from a nationally representative sample of adults where we expect to see broad variability. Now, we wish to study these in a narrow population group (African-American girls in San Francisco). We expect that this narrower population will have an overall lower variability. If so, it may be the case that even the analytes with high ICC, such as total cholesterol, will not be so high when applied to a more narrow population. Thus, if you just assumed that the ICCs would all go down (and that recruiting more subjects to overcome this would not be easy), then it would also be correct to say that we would want consider improving reproducibility on all of them.

## Slide 35: Understanding Measurement: Aspects of Reproducibility and Validity
Reproducibility vs validity of measurements
Focus on reproducibility: Impact of imperfect reproducibility on precision & validity of study inferences
Quantitating reproducibility of interval scale measurements
  Depends upon purpose
    Research
      intraclass correlation coefficient
    Individual use (i.e. individual-level management or classification)
      within-subject standard deviation and “repeatability”
      coefficient of variation
Improving reproducibility
(Estimating validity of measurements -- On Problem Set)
Notes: We mentioned earlier that there are two main purposes for estimating reproducibility. One is for research, but there is another reason, which comes up in clinical management or in individual subject characterization. Let’s now move to the other reason to quantitate reproducibility, which is for individual use.

## Slide 36: Other Purpose in Calculating Reproducibility
In clinical management or individual subject characterization/classification , we often like to know:
Just how different could two measurements taken on the same individual be -- from random measurement error alone?
Not the focus of research/this course, but it is important to know about/distinguish these concepts from research needs
Notes: In clinical management or any situation where the goal is individual subject characterization, the question is: Just how different could two supposedly identical measurements taken on the same individual be, just from random measurement error alone?
Again, this is not the focus of research/this course, but it is important to be able to know about/distinguish these concepts from research needs.
In fact, individual subject characterization does sometimes come up in research. For example, when we enroll people into studies we use inclusion and exclusion criteria, which are indeed measurements we need to make on people. The reproducibility of the measurement will be important in knowing whether the right people got enrolled. The variable may not be one we analyze for its correlation with any outcome but it is nonetheless important to the goals of the project.

## Slide 37: Start by estimating 2E
Can be estimated if we assume:
  mean of replicates in a subject estimates true value
To begin, for each subject, the within-subject variance s2W (looking across replicates) provides an estimate of 2E
s2W
Notes: To address this question, we first estimate the within-subject variability, or the variance term caused by measurement error. Remember, we already had in interest in this when we were evaluating the ICC.
Thankfully, we can get this direct estimate from the data if we are willing to make a reasonable assumption. That is, we need to assume that the mean of measurement replicates on a given subject is an unbiased estimate of their true value. In other words, if you could measure someone over and over again, we could take the mean value as the true value for that measurement.
If this assumption can be made, then the process starts by having each subject provide an estimate of the within-subject variance by looking across replicates in each subject. The within-subject variance, s-squared sub w provides an estimate of sigma squared sub E. The estimate is provided by the within-subject variance. s2W, looking across replicates.
In the peak flow data, for the first subject, the mean value is 492. If you work out the variance of the two values, 494 and 490, you will see that it is 8. You can easily calculate the within-subject variance for each person.

## Slide 38
Common (or mean) within-subject variance (s2W ~ 2E)
Common (or mean) within-subject standard deviation (sw ~ E)
“s” when estimating from sample data
“” when referring to population parameter
s2W
Notes: We can obtain the average of the within-subject variances in our sample data, s2W, to get the best estimate of s2W. If we work through the math it is 8 plus 72 plus all of the rest, divided by 17, equals 234. A note on usage. Because we are estimating this from sample data, we call it “s” squared. It is estimating a population parameter, sigma squared. Try not to be confused by this.
The common or mean within-subject standard deviation is just the square root of the variance. Hence, s sub w is 15.3.

## Slide 39: Impact of 2O on ICC
Scenario | 2O | 2E | ICC
Peak flow data sample | 12,392 | 234 | 0.98
More overall variability | 20,000 | 234 | 0.99
Less overall variability | 1200 | 234 | 0.80
Remember, we used 234 earlier to illustrate the ICC.
Now we know how to calculate it.
Notes: Remember, we used 234 earlier to illustrate how to work with an ICC. Now we know how to calculate it.

## Slide 40
Classical Measurement Theory:
  observed value (O) = true value (T) + measurement error (E)
  If we assume E is random and normally distributed:
    E ~ N (0, 2E)
  Mean = 0
Fraction
error
-3
0
.02
.04
.06
Error
-2
-1
0
1
2
3
Distribution of measurement error
  Variance = 2E
What is 2E estimating?
Notes: This is a slide from earlier that reminds us again what we are looking to estimate, sigma squared sub E, the variance of the random measurement error. Every subject in our dataset who has 2 or more measurements can provide us with an estimate of 2E by looking at each subject’s within-subject variance across replicates. We then find the common within-subject variance.
If we assume that the differences between replicate and the mean value, in other words, the error term, within a given subject is normally distributed, then the within-subject variance we have calculated is the variance for the distribution shown. This is all just another way of saying that we assume that error is random and normally distributed.

## Slide 41: How different might two measurements be from random error alone?
Difference between any 2 replicates for same person = difference = measure1 - measure2
Variability in differences = 2diff (just a definition)
2diff = 2meas1 + 2meas2 (accept without proof)
2diff = 22meas1 (the variability of meas1 and meas2 are the same)
2meas1 is simply the variability in replicates. It is 2E
Therefore, 2diff = 22E
Because s2W estimates 2E, 2diff = 2s2W
In terms of standard deviation:
diff
Notes: Now let’s finish the work that is needed to address the main question: How different might two measurements be from random error alone?
First, some simple math. For any 2 replicates performed on the same person, the difference between the 2 replicates is meas1 minus meas2. The variability of the differences between any 2 replicates is depicted as sigma squared subscript difference, in other words, the variance. This is just a definition. It turns out that we can estimate the variance of the difference (the difference between 2 replicates) if we know the variance of meas1 and meas2. The variance of the difference is simply the variance of meas1 plus the variance of meas2. For now, you’ll need to accept this without proof.
Now, because these measurements are just repeat measurements of the same thing, we know that the variance of meas1 is equal to the variance of meas2. The variance of both measure 1 and measure 2 is, in fact, simply the variance looking replicates. This is the same as the variance of the error term or sigma squared sub E. Therefore, the variance in the differences between any two replicates is just 2 times the variance the error term.
We already in the past few slides showed how the variance of the error term is estimated by the within-subject variance. Therefore, the variance of the differences in replicates is 2 times the within-subject variance.
To speak on the standard deviation scale, we need to take the square root of the variance of differences. When we do this, it boils down to the square root of two times s sub w. The square root of 2 is 1.41. Therefore, the standard deviation of the difference between two replicates is 1.41 times the within-subject standard deviation.

## Slide 42: Distribution of Differences Between Two Replicates
If assume that differences between two replicates:
  are normally distributed and mean of differences is 0
   diff is the standard deviation of differences
For 95% of all pairs of measurements, the absolute difference between the 2 measurements may be as much as (1.96)( diff) = (1.96)(1.41) sW = 2.77 sW
xdiff  0
 diff
(1.96)( diff)
Notes: Let’s look graphically at the distribution of differences between two replicates.
Let’s say we take a zillion pairs of measurements on someone. Let’s say it is height.
If we assume that the distribution of differences between any two replicates for the same person is
- normally distributed
- with a mean of zero
- and some variance sigma,
then we can say, because of the properties of a normal distribution, that the difference between two measurements on the same subject is expected to be less than 1.96 x standard deviation of the difference for 95% of all pairs of measurement. From the last slide we know that the standard deviation of the difference is 1.41 x the within-subject standard deviation. This collapses to 1.96 times 1.41 which is 2.77 times the within subject standard deviation.

## Slide 43: 2.77 sw = Repeatability
For Peak Flow data:
For 95% of all pairs of measurements on the same subject, the difference between 2 measurements can be as much as 2.77 sW = (2.77)(15.3) = 42.4 l/min
i.e., the difference between 2 replicates may be as much as 42.4 l/min just by random measurement error alone.
42.4 l/min termed (by Bland-Altman): “repeatability”, “repeatability coefficient”, “coefficient of repeatability, (CR)”
Notes: So, for the peak flow data, we already estimated that the average within-subject standard deviation was 15.3 l/min.
This means that for 95% of all pairs of measurements on the same subject, the difference between 2 measurements can be as much as 2.77sw = (2.77)(15.3) = 42.4 l/min. Said another way, the difference between 2 replicates may be as much as 42.4 l/min just by random measurement error alone. Bland and Altman refer to this specific derivative of the within-subject deviation as the “repeatability” or “repeatability coefficient” or “coefficient of repeatability” (CR or COR) of the measurement. It is really the most critical derivative of the within-subject standard deviation.

## Slide 44
Is 42.4 liters a lot (poor reproducibility) or a little (good reproducibility)?
A lot (poor reproducibility) - A
Not sure; ask a pulmonologist - C
A little (good reproducibility) - B
Interpreting Repeatability
For new Peak Flow meter:
For 95% of all pairs of measurements on the same subject, the difference between 2 measurements can be as much as 42.4 l/min by random measurement error alone
Notes: 44
Thus, for this new peak flow meter, we know that for 95% of all pairs of measurements of the same subject, the difference between the two measurements may be as much as 42.4 l/min by random error. Is this a lot or a little? In other words, is this poor reproducibility or good reproducibility?

## Slide 45
Is 42.4 liters a lot (poor reproducibility) or a little (good reproducibility)?
A lot (poor reproducibility) - A
Not sure; ask a pulmonologist - C
A little (good reproducibility) - B
Interpreting Repeatability
For new Peak Flow meter:
For 95% of all pairs of measurements on the same subject, the difference between 2 measurements can be as much as 42.4 l/min by random measurement error alone
Notes: 45
I would say that the best answer is to consult a pulmonologist.

## Slide 46: Interpreting “Repeatability”: Is 42.4 liters a lot or a little? Depends upon the context
If other gold standards exist that are more reproducible, and:
  differences < 42.4 are clinically relevant, then 42.4 is bad
  differences < 42.4 not clinically relevant, then 42.4 not bad
If no gold standards, probably unwise to consider differences as much as 42.4 to represent clinically important changes
  would be valuable to know “repeatability” for all clinical tests
Notes: Why do we say to consult a pulmonologist?
How should we interpret 42.4 liters, the repeatability value? We are left with the question of whether 42 l/min is a lot or a little.
This means that any two measurements on the same individual can differ by as much as 42 l/min. Understanding if this is good enough is dependent upon what else is known about the entity that is being measured. For clinical management, if you happen to have other gold standards available, which are more reproducible, then you should know whether differences as large as 42.4 are clinically relevant, in other words do they represent a clinically meaningful difference. If such gold standards exist and you know that say differences of 20 represent a clinically meaningful differences, then the repeatability of 42.4 for this new measurement device is bad. On the other hand, if you have a gold standard and you know that differences of as much as 42.4 l/min really are not associated with any clinical significance, then the 42.4 repeatability of this new device does not represent a problem.
What if no other gold standards exist? Then, given that the same person can have replicate measurements as far a part as 42.4 l/min, then it is clear that you should not necessarily consider any changes up to 42.4 to be clinically relevant. In other words, you would be cautious about making any interventions based on changes up to 42.4 l/min.
That said, wouldn’t it be nice to have the repeatability value for every clinical lab test that is available. Right now, we get a normal range shown with lab values but repeatability would be very useful. Someone should have this be their project.

## Slide 47
Aliu et al. Translational Oncology 2014
Notes: Here is a recent example using repeatability. In this case, normal women underwent two measurements of their breast tissue by MRI. The radiologists in particular are expert in this material. Interestingly, even they lapse into a collection of synonyms when they refer to this entity as “reliability” in the Methods.

## Slide 48: Note on Vocabulary
As a specific metric, several ways to calculate reproducibility:
  For Research
    ICC
  For Individual-level characterization
    Repeatability
    Coefficient of variation
  Best to reserve use of “repeatability” to specific meaning
As a general term, ‘Reproducibility’ has many synonyms
  aka: reliability, repeatability, precision, variability, dependability, consistency, stability
Notes: Now that we have introduced another term, reproducibility, let’s put it into context by remembering the vocabulary.
The concept of reproducibility, as a general term, has many synonyms, such as reliability, repeatability, precision, variability, dependability, consistency, stability. Notice that repeatability is in this list.
When used in a specific sense, there are several ways to calculate reproducibility as we have now discussed. For research, we described the ICC. For individual-level characterization, we just calculated what we called repeatability. We think it is best to reserve use of the term repeatability to this speciic meaning.

## Slide 49: Assumption: One Common Underlying sW
Estimating sw from these subjects appropriate only if just one sW
i.e, sw does not vary across measurement range
Bland-Altman approach: plot mean by standard deviation (or absolute difference)
mean sw
Notes: There is one other assumption we needed to make along the way with these repeatability calculations to have them be valid. That is, we assumed that there was just one within-subject standard deviation that applied to all subjects across the range of values of the measurement. We determined the common within-subject standard deviation by taking a simple average of each individual subject’s within-subject variance and then taking the square root to get the standard deviation. It only makes sense to do this if there is indeed just one within-subject standard deviation that exists and applies to everyone. In other words, it only makes sense if the within-subject standard deviation does not vary across the range of measurements. To assess, we take the Bland-Altman approach of plotting the within-subject standard deviation by the within-subject mean.

## Slide 50
Common (or mean) within-subject variance (s2W ~ 2E)
Common (or mean) within-subject standard deviation (sw ~ E)
“s” when estimating from sample data
“” when referring to population parameter
s2W
If each subject not contributing the same concept to the pooled average, then no point in forming an average.
Notes: Recall that this is important because of the way we calculated the within-subject standard deviation, which was that for each subject we calculated a within-subject mean and ultimately a within-subject variance. If each subject is not contributing the same concept to the pooled average, then there is no point in forming the average.

## Slide 51: Assumption: One Common Underlying sW
Estimating sw from individual subjects appropriate only if just one sW
i.e, sw does not vary across measurement range
Does the within-subject standard deviation vary across the range of data?
mean sw
Notes: Does the within-subject standard deviation vary across the range of data? We don’t have a lot of data to use to evaluate this, but these data show no strong evidence that the within-subject deviation is changing across the range of data. This assessment can just be made by eyeball because you really don’t want to apply statistical testing in that small sample sizes might never show statistically significant differences. We conclude are in pretty good shape with this assumption for the peak flow data (i.e., no strong evidence that the within-subject standard deviation is changing over the range of the data) and thus we can calculate repeatability.

## Slide 52: Another Interval Scale Example
Salivary cotinine in children
n = 20 participants measured twice
From Bland & Altman
Notes: However, let’s look at another interval scale example, and we will again get it from Bland and Altman in which the concentration of cotinine, a metabolite of nicotine, was looked at in the saliva of children to get an idea of their exposure to cigarettes.
So, the structure of the data is 20 children, each with two measurements.

## Slide 53: Cotinine: Within-Subject Standard Deviation vs. Mean
correlation = 0.62
p = 0.001
Appropriate to estimate mean sW?
Error proportional to value: A common scenario in biomedicine
Notes: This time when we plot the within-subject standard deviation by the within-subject mean value, we see a different pattern. What is it? Here, we see that the error is proportional to the mean value. The error gets bigger as the mean value gets bigger. Although this was not the case with the peak flow data, this type of scenario is pretty common in biomedical measurement. Given this scenario, is it appropriate to estimate the mean (common) within-subject standard deviation? No, there is not one single value. Hence, it is not appropriate to try to estimate mean sw as it stands now.

## Slide 54: Solution: Perform Log10 Transformation Work on the Multiplicative Scale
Within-subject standard deviation
Within-Subject mean cotinine
-1
-.5
0
.5
1
0
.2
.4
.6
correlation = 0.07 p=0.7
mean sw
Replotted, now on log10 scale
See Extra Slides for the math and interpretation
Notes: The solution is to log10 transform cotinine. In other words, work on the multiplicative scale. When we work with log transformed data and plot the within-subject standard deviation vs the mean, we see the following figure. Now, we no longer have a relationship between the difference and the mean. To satisfy any of you disbelievers, you can perform a correlation on this scatterplot and see that there is no evidence of an association. As we move across the range of measurement, there is no evidence that the within-subject standard deviation is changing. Note that the variability of the estimate could be changing but that is not the issue.
Therefore, now, it is reasonable to use each of the subject’s within-subject standard deviation as an estimate of the overall within-subject standard deviation.

## Slide 55: Coefficient of Variation (“CV”)
Another approach to expressing reproducibility for individual subject-level characterization if sw is proportional to value of measurement (e.g., cotinine data)
Depicts error in context of overall magnitude of measurement
Calculations found in S & N text and in Extra Slides
For completeness, we include:
Favored among lab scientists
Hard to interpret, other than we want it low
We often backcalculate it to ‘repeatability’
Notes: For completeness, we will also describe another approach that can be used to express reproducibility when you have data where the within-subject standard deviation is proportional to the mean. This is an entity called the coefficient of variation, often abbreviated as CV. The CV depicts within-subject error in the context of the overall magnitude of the measurement. The CV is the within-subject standard deviation divided by the within-subject mean.
We won’t go into detail about the calculation other than to say that it is pretty simple. One calculates a within-subject CV for each person and then calculate the mean. Then you form the ratio. The details can be found in the S and N text as well as the extra slides for this lecture.
Historically, this is a metric that has been favored among lab scientists. We, however, actually it hard to interpret because it is not on the native scale. All we know is that we want it to be low. In fact, we often find ourselves trying to use it to backcalculate to the more useful ‘repeatability’ metric. Nonetheless, we mention it because you will see it in the literature when describing reproducibility.
-----------------
By saying that the within-subject standard deviation is proportional to the value of the measurement, we are saying that the within-subject standard deviation is equal to K times the within-subject mean value. K is the coefficient of variation. In other words, K is the within-subject standard deviation divided by the within-subject mean.

## Slide 56
Notes: This table summarizes the indices that are useful in quantitating reproducibility. It is organized by purpose and the pattern of the within-subject variability across the range of data.
When the purpose is to evaluate whether the reproducibility is suitable for research vs when more tightening of the measurement’s reproducibility is needed, we talked about the intraclass correlation coefficient, ICC. It can be used regardless of the pattern of the within-subject standard deviation is over the range of the measurement.
When the purpose is looking at individual measurements in individual persons (i.e., individual-level characterization), when the within-subject variability is constant across the range of data, as it was in the peak flow data, repeatability is the most useful index. If the within-subject variability is proportional to the magnitude of the measurement, as it was with the cotinine data, repeatability is also the way to go, but you need to work with the data on the log, or ratio, scale. A coefficient of variation is also acceptable here, although we think it is less useful.
We did not directly discuss this but when your data does not behave nicely, meaning the within-subject variance is neither constant nor proportional to the mean value, you’ve got a problem. This does not commonly happen in biology, however. If it does occur, one of the simple things you can do is to break up the range of data into smaller pieces where the within-subject standard deviation is either constant or proportional to the mean. Then, in each of these segments you can report the repeatability. In the end, you will end up with a family of such indices.

## Slide 57: Understanding Measurement: Aspects of Reproducibility and Validity
Reproducibility vs validity of measurements
Focus on reproducibility: Impact of imperfect reproducibility on precision & validity of study inferences
Quantitating reproducibility of interval scale measurements
  Depends upon purpose
    Research
      intraclass correlation coefficient
    Individual use
      within-subject standard deviation and repeatability
      coefficient of variation
Improving reproducibility
(Problem set: estimating validity of measurements)
Notes: For the remainder of the session, let’s discuss how to improve reproducibility.

## Slide 58: How to Increase Power?
Assume for skin fold thickness have a SD of 1.5 and ICC, in your population, is 0.7
What should you do to increase power?
Increase subjects in each group - A
More standardization of outcome measurement - E
Make multiple measurements/subject - C
Increase effect size - B
Find more homogeneous subjects - D
Evaluation of skin fold thickness in 2 diet groups
Effect size = 0.4 units
Plan: 100 subjects in each group
Alpha = 0.05
Standard deviation (SD) of skin fold thickness
Notes: 58
Let’s start by looking back at the example we gave earlier where we were evaluating skin fold thickness, the outcome variable, in 2 groups. Let’s say this is a study of nutrition where we are comparing two diets for their effects on skin fold thickness. Let’s say that we plan initially to study 100 subjects in each group and our desired effect size is 0.4 units. If we set alpha (the type I error) at 0.05, this plot shows the relationship between the standard deviation of skin fold thickness in the study population and statistical power – if we study 100 subjects in each group. Let’s say that we have a standard deviation of 1.5 in our measurement of skin fold thickness and the ICC, in your population, is 0.7. This translates to power of just above 50%, which is pretty bad. What should you do to increase power?

## Slide 59: How to Increase Power?
Assume you have a SD of 1.5 and ICC is 0.7
What should you do to increase power?
Increase subjects in each group - A
More standardization of outcome measurement - E
Make multiple measurements/subject - C
Increase effect size - B
Find more homogeneous subjects - D
Both C and E work by improving reproducibility
Standard deviation (SD) of skin fold thickness
All answers are technically correct, but some are more efficient/elegant than others.
Notes: 59
All of these answers are technically correct, but some are more efficient and elegant than others. While you COULD try any of answers A to E, the best answers are C, which is to make multiple measurements per subject, and E, which is further standardize the outcome measurement, skin folk thickness. Increasing subjects is acceptable in that increasing subjects virtually always increases power, but this is not cheap or easy. Increasing the effect size is also a fool proof way to increase power but not a very smart one. By limiting yourself to just be able to detect large effects may result in a very wasteful study that could not pick up smaller but nonetheless clinically relevant effects. Finding more homogeneous subjects would work but it may not be easy or desirable.

## Slide 60: For any given sample size, effect size, and alpha, to increase power, need to decrease one or both of the components of 2O
2O = 2T + 2E
Standard deviation (SD) of skin fold thickness
Decreasing 2T requires finding a more homogeneous population
  Often not easy
  Diminishes generalizability
ICC tells us whether it is worthwhile to try to decrease 2E
Notes: 60
To better understand this, as a review, remember that the total observed variance (which is standard deviation squared) is equal to the sum of the true between-subject variability and the within-subject variability (or random measurement error). For any given sample size, effect size, and alpha, to increase power, one needs to decrease one or both of the components of 2O.
Decreasing 2T requires finding a more homogeneous population. This may not be easy in practice. It also diminishes generalizability.
The ICC tells us whether it is worthwhile to try to decrease 2E.

## Slide 61
ICC
0.5 0.6 0.7 0.8 0.9 1.0
N = 25 per group N = 50 per group N= 100 per group
Effect of ICC on Sample Size
2 group study
Continuous outcome variable
Perkins et al. Biol. Psych. 2000
Rule of thumb: Moving from 0.7 to 0.9 reduces sample size by 22%
Less is gained by attempting to improve ICC >0.9
Notes: Looked at in terms of impact of ICC on sample size, we see this plot. For any fixed effect size and fixed alpha, you will need more subjects with a smaller ICC. In other words, you need fewer subjects with higher ICCs. For example, a study that used 100 subjects per group with a measurement with an ICC of 1.0 would require 143 subjects if the ICC was 0.7. Moving from 0.7 to 1.0 could result in not needing 43 subjects in each group. Rule of thumb: moving from 0.7 to 0.9 reduces sample size needs by 22%. And, little is gained when attempting to improve upon an ICC of 0.9 or greater.

## Slide 62: Improving Reproducibility (i.e., Increasing ICC)
Standardize performance of the measurement
  Perform it same way each time
  Determine sources of random error
    Think through the steps
Notes: So, how do we improve reproducibility? Often, the cheapest and easiest thing to do first is to standardize the performance of the measurement. This means perform it the same way each time. The process starts with determining the sources of random error, which means thinking thru the steps of how the measurement is made.

## Slide 63: Determine Sources of Random Error: What contributes to 2E ?
The observer (the person who performs the measurement)
    within-observer (intrarater)
    between-observer (interrater)
Instrument
    within-instrument
    between-instrument
Importance of each varies by study
Notes: For any measurement, think about the sources of error.
In terms of the observer, the person making the measurement, there may be variability within a given observer and or between observers.
Many measurements, like biological measurements, require an instrument. Here, too, we may see within-instrument and between instrument variability.
The importance of each of these varies by study. If you have several different field staff drawing blood and this blood is being tested with several different instruments, then you have the opportunity to have all four of these. On the other hand, if your measurement is being performed by just one observer - say an interview - and does not require an instrument, then you would only have to contend with within-observer error.

## Slide 64: Sources of Random Measurement Error
e.g., plasma HIV RNA level (amount of HIV in blood)
  observer: measurement-to-measurement differences in blood tube filling (diluent mix), shaking/mixing of tube; temperature in transit; time before lab processing
  instrument: run-to-run differences in reagent concentration, PCR cycle times, enzymatic efficiency
Each of these can be standardized to reduce variability
Notes: Let’s take an example from the HIV field by looking at the measurement of HIV, the virus, in blood, which is known as plasma viral load. There may be more steps in the process than you realize.
On the observer side, there may be differences from measurement to measurement in how much blood is put in the vacutainer tube and thus what kind of dilution occurs after mixing with the diluent. There may also be measurement to measurement differences in how long the tube sits at room temperature before processing. Sitting at room temperature allows for cell-associated virus to leach out and contaminate the plasma. It may also cause degradation of plasma HIV RNA.
On the instrument side, the plasma now has to go through a series of processing steps and then through PCR where it encounters all sorts of variability like reagent concentration, enzymatic efficiency, cycle times, and temperature.
If we add all of these up, the variability could become large.

## Slide 65: Improving Reproducibility
Standardize performance of the measurement
  Perform it same way each time
  Determine sources of random error
    Think through the steps
  Training and Standard Operating Procedures (SOPs)
    Not a bureaucratic hassle; instead, an important tool
  Automation
    Machines less apt to make random errors than humans
Notes: The solution to performing something the same way each time is training of research staff and creation of standard operating procedures, known as SOPs. These are often dreaded words in research because they often denote some kind of forced bureaucracy from investigators to staff. Instead, it is important to make people understand why these are important, which is to improve reproducibility. Finally, automation – use of machines – will improve reproducibility, because machines make random errors less often than humans.

## Slide 66: Improving Reproducibility
Standardize performance of the measurement
  Perform it same way each time
  Determine sources of random error
    Think through the steps
  Training and Standard Operating Procedures (SOPs)
    Not a bureaucratic hassle; instead, an important tool
  Automation
    Machines less apt to make random errors than humans
Perform replicates and use the mean value as “final”
Notes: Besides standardization the other approach to improve reproducibility is to perform replicate measurements.

## Slide 67
If just one replicate used as final value per subject
Poor reproducibility
Good Reproducibility
Taking the average of replicates of a measurement with poor reproducibility increases reproducibility
If mean of several replicates used as final value
Notes: Why does taking multiple measurements per subject work to increase reproducibility? I re-inserted this slide with the targets to graphically illustrate. If you have a measurement with intrinsically poor reproducibility and you took just one replicate measurement on each subject as his/her final value, this is what the measurement would look like on the left. Instead, if for each person you took the mean of several replicates, you would have the picture on the right. As long as the error is random, taking several measurements will, on average, result in a value that is closer to the truth than any single value and a collection of these means of replicates will be closer together than a collection of single measurements..

## Slide 68
Number of replicates
ICC
Perkins et al. Biol. Psych. 2000
How many replicates are needed?
Spearman-Brown formula
Assume that ICC for 1 replicate (i.e., no averaging) =
Greatest yield is for 1 or 2 additional replicates
Then begins to level off, unless you started very low
Notes: How many replicates does it take to improve reproducibility? The answer comes from what is known as the Spearman-Brown formula, but we won’t take the time to derive it. The answer depends in part upon where you start with just taking 1 replicate. If we focus on a measurement with an ICC of 0.7 if you just used one replicate (i.e., no averaging of values), you can bring this up to 0.8 by taking 2 replicates and used the mean of the two as the “final” value. You will need 4 replicates to get it to 0.9.

## Slide 69: To increase power: More subjects or better measurements?
Depending upon the ICC and costs per test, performing more replicates often more cost-effective than adding more subjects
Remember: each new subject requires the full suite of measurements to be performed, even the fully reproducible ones.
  Instead, keep subjects fixed and make replicates where needed
See Extra Slides for simulation study
Notes: The bottomline is that it is often the case that performing more replicates is often more cost-effective than adding more subjects. This depends upon a number of factors, but it should definitely be considered. Most investigators will instinctively grab for more subjects, but it is often more efficient to perform more replicates.
Remember, when you add more subjects, you need to make all of the measurements even the ones that are fully reproducible. Instead, consider the efficiency when you keep the number of subjects fixed and make replicates where needed.
The Extra Slides show a simulation study which illustrates this point.

## Slide 70: Practical Implications for Research
Understand your measurements
Planning research
  Do your measurements need improvement?
    SOPs; more automation; replicate measurements
  Is it feasible for them to be improved?
  Describe reproducibility and validity in grant proposals
Presenting research
  Describe reproducibility & validity of key measurements in Methods section
Notes: In ending, what does all of this mean for you in terms of practical implications for research?. This is not just a bunch of theory, but, in fact, there are important messages here for research.
The main message is that you need to understand your measurements. In terms of planning research, how this starts is asking whether the available measurements meet some bare minimum adequacy. I cannot tell you exactly what that is but between this week’s material and next week’s material, hopefully you will be become to spot an inadequate measurement when you see one. If the measurements are useable, do they need improvement? We talked about the ways we can improve reproducibility which are the use of SOPs, more machine automation (typically more reproducible than humans); and the use of replicate measurements. Of course, if they need improvement, is it feasible to actually do so? Finally, the best reviewers will expect you to describe the reproducibility and validity of your measurements in grant proposals.
In terms of presenting research, there is not much you can do after the work is done (although we will describe some next week) but you should consider describing the reproducibility and validity of key measurements in Methods sections.

## Slide 71: Summary
Characteristics of a measurement: Reproducibility vs validity
Measurement reproducibility has key role in influencing precision and validity of inferences in our different study designs
Quantitation metric of reproducibility depends upon scale and purpose
  Interval scale
    For research purposes, use ICC (but it is population-dependent)
    For individual-level use, calculate repeatability (or CV)
  (For categorical scale measurements, use Kappa)
Improving reproducibility can be done by finding/reducing sources of error, SOPs, automation and by multiple measurements (replicates)
Assessment of validity depends upon whether or not gold standards are present, and can be a challenge when they are absent
Notes: To conclude, let me highlight the following points.
We’ve defined and contrasted the most important characteristics of a measurement, reproducibility vs validity.
We’ve spent most of the session on reproducibility, especially showing its impact on the precision of down the line study inferences. We’ve also mention its affect on validity and we will do more of this next week.
When estimating reproducibility (i.e., choosing the metric), you need to keep in the mind your purpose and your measurement scale. We really only discussed interval scale measurements today. When asking the question in research whether your measurement is suitable or it needs more work in improving reproducibility, we talked about the intraclass correlation coefficient. When you need to understand reproducibility for individual-level characterization, use repeatability, as described by Bland and Altman. A coefficient of variation can be useful in some situations. There is no role for the Pearson correlation coefficient.
Improving reproducibility starts by finding and reducing the sources of error. Use SOPs and increase machine automation. If you cannot make standardization improvements, then taking multiple measurements (i.e., replicates) will improve reproducibility.
We did not discuss categorical scale measurements today, but those of you taking the Clinical Epidemiology course already learned about this in the form of Kappa.
Finally, although we won’t have time to discuss this in class, the assessment of validity starts with whether gold standards are present. If some empirical criterion is available, the methods of assessment very closely follow the pattern we used for assessing reproducibility. You will have a chance to practice in the homework this week. When gold standards are absent, things can get very challenging.

## Slide 72: Notes on Problem Set
Several short methodological articles in Required Reading
  These explain the concepts better than any textbook we know of
  Gives you practice reading methodologic articles
  Reminds us that methods are evolving
Be sure to distinguish between 3 tasks/purposes, which are the determination and interpretation of:
  Reproducibility of a measurement
  Agreement between methods of measurement (“Method agreement”)
  Validity of a measurement
All 3 tasks have much in common numerically but have different goals & slightly different mathematical techniques
Notes: A few notes on the Problem Set for this week. There are several short methodological articles in the Required Reading that you will need to cover in order to complete the problems. We are asking you to read these because they cover the concepts better than any textbook that we are aware of. And, reading these will give you some practice reading methodologic articles. This is a practice you will do during your career. It also reminds us that methods are evolving and the evolution is done initially through the scientific literature, not through textbooks.
These articles cover three basic tasks/concepts which are sometimes easy to get confused. They are:
Determination of the reproducibility of a measurement. This is largely what we covered today in class.
Agreement between two or more methods of measurement. This is called Method Agreement.
And
Validity of a measurement.
All 3 of these have much in common but they do have different goals and slightly different mathematical techniques. It is important when doing the problems to stay focused on which of the 3 you seek to estimate.

## Slide 73: Extra Slides

## Slide 74: Estimating Repeatability for Cotinine Data Logarithmic (base 10) Transformation
Notes: Use of log10 transformation on the aforementioned salivary cotinine data. We can overcome the problem of dependence of standard deviation on the underlying value by working on the multiplicative scale. To do this, what one does is simply obtain the log base 10 of both the results of trial 1 and trial 2 and work with these numbers as logarithms. Remember that a 1 unit difference on the log10 scale is a 10 fold ratio.

## Slide 75: sw for log-transformed cotinine data
sw
because this is on the log scale, it refers to a multiplicative factor and hence is known as the geometric within-subject standard deviation
it describes variability of replicates in ratio terms (rather than absolute numbers)
Notes: Working with the data in their log-transformed state, we do with it exactly what we did before. We can estimate the common within-subject standard deviation, either by working through the numbers or by using an ANOVA table, and it is 0.175.
However, you have to remember (and sometimes this takes some thinking in a quiet room) that this is on the log 10 scale where every unit is a factor of 10, not 10 more units but 10 times the prior unit. Hence, this is known as a geometric within-subject standard deviation.
Hence, in the prior examples, we described variability and variances and standard deviations of the replicates in terms of absolute differences. A geometric within-subject standard deviation describes the variability the replicates in terms of ratios (or factors).

## Slide 76: “Repeatability” of Cotinine Measurement
The difference between 2 measurements for the same subject is expected to be less than a factor of (1.96)(sdiff) = (1.96)(1.41)sw = 2.77sw for 95% of all pairs of measurements
For cotinine data, sw= 0.175 log10, therefore:
  2.77*0.175 = 0.48 log10
  back-transforming, antilog(0.48) = 10 0.48 = 3.1
For 95% of all pairs of measurements, the ratio between the measurements may be as much as 3.1 fold
Notes: Just as we did with the peak flow data, we can also estimate the repeatability of the cotinine measurement.
Remember from the peak flow data that the difference between 2 measurements for the same subject is expected to be within 1.96 times the standard deviation of the difference for 95% of all pairs of measurements. And, remember that the standard deviation of the difference between 2 measurements is the square root of two times the within-subject standard deviation. 1.96 times 1.41 is 2.77 and so this boils down to 2.77 times the within-subject standard deviation.
For the cotinine data, the within-subject standard deviation is 0.175 log10 units. Therefore, 2.77 times 0.175 is 0.48 log10 units. Back transforming, this is 10 to .48 power or 3.1.
In words, this means that for 95% of all pairs of measurements, the ratio between the measurements may be as much as 3.1 fold. Again, remember that this difference between measurements that may be caused by measurement error alone is called the “repeatability” of the measurement.

## Slide 77: Cotinine: Within-Subject Standard Deviation vs. Mean
correlation = 0.62
p = 0.001
Coefficient of variation quantifies the proportion
Error proportional to value:
A common scenario in biomedicine
Notes: The metric called the coefficient of variation can also be used when the within-subject standard deviation varies according to the range of the data. The cotinine data is one such situation. The CV quantifies the ratio of the within-subject standard deviation to the within-subject mean.

## Slide 78: Coefficient of Variation (CV)
Another approach to expressing reproducibility if sw is proportional to the value of measurement (e.g., as seen in cotinine data)
If sw is proportional to the value of the measurement:
sw = (k)(within-subject mean)
k = coefficient of variation
Notes: By saying that the within-subject standard deviation is proportional to the value of the measurement, we are saying that the within-subject standard deviation is equal to K times the within-subject mean value. K is the coefficient of variation. In other words, K is the within-subject standard deviation divided by the within-subject mean.

## Slide 79: Calculating Coefficient of Variation (CV)
At any level of cotinine, the within-subject standard deviation due to measurement error is 36% of the value
Notes: We determine the coefficient of variation using the same logic we used to determine the mean within-subject standard deviation. We first calculate the CV in each subject, as shown in each row here. We then take the simple average. In this case the CV is 0.36. We would say that at any level of cotinine, the within-subject standard deviation due to measurement error is 36% of the value.

## Slide 80: Coefficient of Variation for Peak Flow Data
When the within-subject standard deviation is not proportional to the mean value, as in the Peak Flow data, then there is not a constant ratio between the within-subject standard deviation and the mean.
Therefore, there is not one common CV
Estimating the “average” coefficient of variation (within-subject sd/overall mean) is not meaningful
Notes: What is the coefficient of variation for the peak flow data?
Recall that the within-subject standard deviation was not proportional to the mean level for the peak flow data; in fact, the standard deviation was constant throughout the range of data.
Therefore, there is not one ratio between sw and the mean, and therefore there is not one coefficient of variation.
You could still attempt to calculate a coefficient of variation for the peak flow data ,as is often done, but this does not give you anything meaningful.

## Slide 81: Pearson Correlation: One Metric Not to Use!
Don’t use simple (Pearson) correlation for quantitation of reproducibility
Historically, most common in literature and still very much in use, but least useful for a variety of reasons
Notes: There is one metric not to use when quantifying reproducbility, and that is the Pearson Correlation Coefficient (i.e., simple correlation). We only mention it because it has been used most commonly in literature is still very much in use but it is least useful for a variety of reasons. You can read more about this in the Required Reading.

## Slide 82: Don’t Use Simple (Pearson) Correlation for Assessment of Reproducibility
Too sensitive to range of data
  Correlation is always higher for greater range of data
Depends upon ordering of data
  get different value depending upon classification of meas 1 vs 2
Importantly: It measures linear association only
  it would be amazing if the replicates weren’t related
  association is not the relevant issue; numerical agreement is
Most common approach but least meaningful
Notes: Reasons not to use the Pearson Correlation Coefficient as a metric for reproducibility.
If you learn nothing else from today’s session, please remember not to use simple correlation coefficients for the assessment of reproducibility. I’m not going to go into lengthy detail on this because the reasons for this are nicely described in the Bland-Altman articles as well as in the Szklo and Nieto text. The highlights of the argument are listed here and they include that the Pearson correlation coefficient is sensitive the range of data with correlation always higher for a greater range of data. Strangely, the correlation coefficient depends upon the ordering of the data. You can get different values depending upon whether you call a replicate measure 1 or measure 2.
More importantly, let’s think a moment about what the correlation coefficient is actually saying. It is a measure of how the two replicates are associated and in particular how they are linearly associated. But is this really what we want? No, what we want is to see how closely they agree with each other and if this sufficient for our clinical and research purposes. Association is not the relevant issue. Magnitude of numerical agreement is the relevant issue. In a situation of measuring reproducibility, we know that the replicate measurements were done measuring the same property. We would amazed if the two measurements weren’t associated!
Finally, let me give you one more reason not to use correlation coefficients to assess reproducibility. That is, at the end of the day it does not tell us an answer in the same scale as the measurement is made and therefore really does not tell us the magnitude of reproducibility in clinical terms. For the peak flow data, what does rho = 0.7 vs 0.8 vs 0.9 mean in the context of peak flow measurement which ranges from 200 to 600? This is especially problematic when the context is individual subject-level characterization.

## Slide 83
Effect of ICC on Power
2 groups of 100
Continuous outcome variable
Perkins et al. Biol. Psych. 2000
Effect Size
ICC
Notes: Another plot of the importance of ICC on statistical power. For a give effect size, power increases with an increase of ICC. Let’s say we have our 2 group study and 100 subjects per group. On the X axis is power and effect size is on the y axis. The 4 lines shows 4 different scenarios for the ICC of the skin fold thickness measurement. As we move from an ICC of 1.0 to 0.5, power moves from 80% to about 50%.

## Slide 84
Depending upon the ICC, performing more replicates often more cost-effective than adding more subjects

## Slide 85
Simulation study (N=1000 runs) looking at the association of a given risk factor (exposure) and a certain disease.
Truth is an odds ratio= 1.6
R= reproducibility of risk factor measurement = ICC
Metric: probability of estimating an odds ratio within 15% of 1.6
Phillips and Smith, J Clin Epi 1993
R = 0.5
R = 0.6
R = 0.8
Probability of obtaining an odds ratio within 15% of truth
R = 1.0
Notes: To address this, these authors performed a simulation study where they were looking at whether a given risk factor was associated with a certain disease. A simulation study means no real data but instead the investigators make up a population on a computer with a specific structure and then they take samples of the population as if they were doing an actual study. They created the population such that the odds ratio for disease was 1.6 (i.e., every unit increase in the risk factor is associated with 1.6 greater odds to develop the disease). They then looked at the influence of reproducibility, which they call R, in the measurement of the risk factor and which they varied from 0.5 (50%) to 1.0 (100%), based on the formula on the last slide. They then performed 1000 simulations of the study, which means they had the computer create 1000 different samples of subjects of given sample size (shown here as No. of subjects). What they evaluated as their metric was the percentage of times the 1000 different study samples were able to detect an odds ratio within 15% of 1.6. In their basecase scenario, they started with a sample size of 5000 subjects and they assumed that 500 people developed the outcome in question (the number of events) and, in the base-case scenario, only one measurement was made of the risk factor on each subject. With this sample size, when the measurement of the risk factor had 100% reproducibility, nearly all of 1000 simulations could always detect a risk ratio within 15% of 1.6. However, as reproducibility fell, the chances of the study simulations detecting an odds ratio close to 1.6 fell dramatically. Note that at 50% reproducibility, a study had only about a 30% chance of detecting an odds ratio 15% within 1.6.
You don’t want this to be you!

## Slide 86
R = 0.5
R = 0.6
R = 0.8
Probability of obtaining an odds ratio within 15% of truth
R = 1.0
Impact of taking 2 or more replicates and using the mean of the replicates as the final measurement
Phillips and Smith, J Clin Epi 1993
Notes: They go on to show, which is actually the main point of their paper, that when reproducibility is low, you would actually do better to take more repeated measurements on fewer people and use the mean of the replicates as the final measurement for each person. Look what happens when they are dealing with a reproducibility of 0.5. When the sample size is halved but two measurements of the risk factor are taken for each person and you take the mean of the two measurements as that person’s final value, the ability of the study design to be within 15% of the truth value is increased enormously. This may seem counterintuitive to some because many people have been taught solely to increase sample size to overcome noisy variables. Well, in fact, in many cases, you would do better to spend your money in tightening up the reproducibility of your measurements or by taking more than one measurement per person and then take a mean, thus achieving the same effect.

## Slide 87: Understanding Measurement: Aspects of Reproducibility and Validity
Reproducibility vs validity of measurements
Focus on reproducibility: Impact of reproducibility on validity & precision of study inferences
Estimating reproducibility of interval scale measurements
  Depends upon purpose
    Research
      intraclass correlation coefficient
    Individual use
      within-subject standard deviation and repeatability
      coefficient of variation
Improving reproducibility
(Estimating validity of measurements – see Extra Slides/Problem Set)
Notes: We will have the opportunity to cover the estimation of validity of measurements in the Problem Set for this week.

## Slide 88: Estimating Validity
Gold standards available
  Criterion validity (aka empirical)
    Concurrent (concurrent gold standards present)
      Interval scale measurement: 95% limits of agreement
      Categorical scale measurement: sensitivity & specificity
    Predictive (gold standards present in future)
Gold standards not available
  Content validity
    Face validity
    Sampling validity
  Construct validity
formulaic
No formulae; much harder
Notes: When estimating validity, the first order of business is determining whether there are gold standards available for the construct under study. If there are, we call the process one of evaluating criterion validity. The process is formulaic. Which formula to use depends upon the nature of the measurement, interval scale or categorical scale. In the problem set, we will practice the estimation of 95% limits of agreement as they relate to interval scale measurements.
If gold standards are not present, then things get more murky and more subjective. This gets at why some of you may have been wondering why we have you do reading from a social sciences textbook for the required reading. We are asking you to do this reading for a couple of reasons. First, to show you that there are some people who give this field of measurement some very serious thinking. When you want to really understand measurement consult with a social scientist because the nature of the measurements in this field has made researchers grapple with these issues on a daily basis. The second reason is that people in biomedicine are not as removed from some of the problems of social scientists as they might think. For example, there are many things that are included regularly in biomedical studies like depression and quality of life that are not immediately measurable with a machine and for which no gold standards exist. It is for this reason, we want to make sure you are familiar with the terminology because you should know how each of the measurements in studies you do have been validated and some of your measures may have been validated using some of the concepts in the article for today.
We’re not going to get deep into this subject in this course, but I wanted to at least provide this outline. When gold standards are not present, we must look at what are called content validity and construct validity.

## Slide 89: Estimating Validity of Interval Scale Measurements - When Gold Standards are Present
Just as we did when evaluating reproducibility in the context of individual subject-level characterization:
  Examine Bland-Altman plots of within-subject differences (new minus gold standard) by the gold standard value
Determine mean within-subject difference (“bias”)
Determine range of within-subject differences - aka “95% limits of agreement”
Practice in Problem Set
Notes: A few details on the estimation of validity on an interval scale measurement when gold standards are present. The first thing to do is just the same as we did when evaluating reproducibility in the context of individual subject-level characterization. That is, we plot the within-subject differences on the y axis against a single value on the x. In this case, use the gold standard value.
The approaches to reproducibility and validity are so similar it is sometimes easy to get to lost. The important thing is to focus on what the task is: reproducibility, validity (comparison vs gold standard), or method agreement.

## Slide 90
Yes - A
Need more information - C
No - B
After competing for years under a cloud of suspicion, Jones tested positive for EPO June 23. Jones immediately requested a repeat test be performed on her specimen (a "B" sample). Her attorney released a statement on Wednesday that the second test was negative, a result that cleared Jones of allegations of use of performance-enhancing drugs.
Should Jones have been cleared on the basis of the B sample?
Olympian Marion Jones Cleared: B Sample Negative
Thursday, September 7, 2006
Notes: 90
Should the athlete have been cleared on the charges based upon the B sample result?

## Slide 91
Yes - A
Need more information - C
No - B
After competing for years under a cloud of suspicion, Jones tested positive for EPO June 23. Jones immediately requested a repeat test be performed on her specimen (a "B" sample). Her attorney released a statement on Wednesday that the second test was negative, a result that cleared Jones of allegations of use of performance-enhancing drugs.
Should Jones have been cleared on the basis of the B sample?
Olympian Marion Jones Cleared: B Sample Negative
Thursday, September 7, 2006
Two different answers (on first and repeat assays) likely an expression of lack of reproducibility (random measurement error)
Only the mean of multiple replicates provides more valid response
Jones later admitted to PED use
Notes: 91
The answer is that this athlete should not have been cleared. I hope now that most everyone can see that the two different answers on the tests (on the first and then the repeat) are likely an expression of random measurement error. You cannot necessarily believe the first answer as truth or the second answer as truth in the face of lack of reproducibility. The fact that one of the results was positive means that this is smoke, and where there is smoke there may be fire (although not necessarilty). It is interesting how we often get an initial positive result test and then perform a repeat test and, if that repeat test is negative, we take the repeat negative as final. This might be the correct approach if there is a strong prior probability that the subject does not have the condition under study but it is not the correct approach if there is equipoise. It is only the mean of multiple replicates that can get you close to the true valid answer. Of note, Jones later admitted to use of performance enhancing drugs.